SHREWSBURY BOROUGH

YORK COUNTY, PENNSYLVANIA

ORDINANCE NO. 2009-4

AN AMENDED AND RESTATED ORDINANCE OF SHREWSBURY BOROUGH, YORK COUNTY, PENNSYLVANIA, ESTABLISHING A WELLHEAD PROTECTION OVERLAY DISTRICT, PROVIDING FOR THE REGULATION OF LAND USES WITHIN SUCH OVERLAY DISTRICT FOR THE PURPOSE OF PROTECTING GROUNDWATER SUPPLIES, PROVIDING FOR REPORTING REQUIREMENTS FOR CERTAIN REGULATED LAND USES WITHIN THE WELLHEAD PROTECTION OVERLAY DISTRICT, AND ESTABLISHING THE MEANS FOR ENFORCEMENT OF THE ORDINANCE.

WHEREAS, Section 1428 of the Federal Safe Drinking Water Act Amendments of 1987 requires that each state develop a program to protect wellhead areas of public water supplies; and

WHEREAS, the Pennsylvania Department of Environmental Protection (PA DEP) has developed a wellhead protection program, which provides that local governments have the responsibility for developing programs including regulations and management controls to protect public water supplies from contamination; and

WHEREAS, the groundwater underlying the community water supply Wellhead protection area is the sole source of Shrewsbury Borough’s existing and future water supply, including drinking water; and

WHEREAS, the groundwater systems supplying the community water supply wellhead protection areas with groundwater are integrally connected with numerous surface waters and streams; and

WHEREAS, accidental spills and discharges of toxic and regulated substances can threaten the quality of such water supplies, posing public health and safety hazards; and

WHEREAS, unless preventive measures are adopted to control the discharge and storage of toxic and regulated substances within the Community water supply wellhead protection areas, further spills and discharges of such materials will predictably occur and with greater frequency and degree of hazard by reason of increasing land development, population and vehicular traffic within the wellhead protection area; and

WHEREAS, unrestrained land development patterns can deplete the available groundwater supply through excess demand, threaten its quality through wastewater pollution, and inhibit the recharge capability of the area through exorbitant impervious areas and competing resource utilization,

NOW THEREFORE, be it enacted and ordained and it is hereby enacted and ordained by the Borough Council of Shrewsbury Borough as follows:

SECTION 1.   PURPOSE AND INTENT: AUTHORITY

- The purpose of this Ordinance is to protect the public health, safety and welfare through the preservation of the groundwater resources of the Borough public water supplies and to ensure a future supply of safe and healthful drinking water for the residents of the Borough.  The designation of the Wellhead Protection Overlay District, as provided herein, and the regulation of activities within such Wellhead Protection Overlay District will reduce the potential for ground and surface water contamination and overuse and thereby preserve irreplaceable groundwater resources.  The delineation of the Wellhead Protection Overlay District and the development of the provisions of this Ordinance are based upon a professional study of land uses hydrology, hydrogeolic and other elements of the area in which Borough water supplies are situated.

- This Ordinance is enacted pursuant to the authority contained in the Constitution of the Commonwealth of Pennsylvania and the Pennsylvania Municipalities Planning Code, Act 247 of 1968, as amended, which provisions authorize the Borough to enact ordinances regulating development and land uses to (i) ensure the public health and safety, (ii) provide a safe, reliable and adequate water supply, and (iii) preserve natural values and aquifers.

(c)   It shall be the responsibility of any person owning real property and/or owning or operating a business within the Borough of Shrewsbury to make a determination of the applicability of the Wellhead Protection Overlay District as it pertains to the property and/or business under his/her ownership or operation, and his/her failure to do so shall not excuse any violations of said sections.

SECTION 2.      ESTABLISHMENT AND DELINEATION OF WELLHEAD

PROTECTION OVERLAY DISTRICT AND WELLHEAD

PROTECTION ZONES

The “Wellhead Protection Overlay District” shall be defined as that area within the corporate boundaries of the Borough as is set forth on the map attached hereto, marked as Exhibit “A” and incorporated herein by reference thereto.  Within the Wellhead Protection Overlay District, the following Wellhead Protection Zones are hereby established:

- Zone 1 shall be that area marked on Exhibit “A” as Zone 1, which Zone 1 represents a protective zone immediately surrounding a community water supply well, which shall be a radial distance calculated on the basis of the specific characteristic of the respective well.

- Zone 2 shall be that area marked on Exhibit “A” as Zone 2, which Zone 2 represents an area determined to be the Zone of groundwater contribution to the well, and

- Zone 3 shall be that area marked on Exhibit “A” as Zone 3, which Zone 3 represents the area that directly contributes surface and groundwater to Zone 2.

Where the boundary of any Zone divides any property, the entire property shall be considered to lie within the Zone offering the highest degree of protection to groundwater resources.  Should any person challenge the boundary of Zones 1, 2 or 3, it shall be the responsibility of that person to retain a Licensed Professional Geologist with competence in the field of hydrogeology to determine the precise boundary of the disputed area.  Upon receipt of the determination, the final boundary to be used will be determined by the Borough with assistance from the Borough Engineer and/or a Licensed Professional Geologist, as appropriate.

SECTION 3.     REGULATED LAND USES

Within the Wellhead Protection Overlay District, land uses shall be regulated as follows:

- Lots and tracts of land located within the Wellhead Protection Overlay District, as delineated on Exhibit “A”, shall be governed by the restrictions applicable to the Wellhead Protection Zone in which such lots and tracts of land are located.

- Certain land uses within the Wellhead Protection Overlay District shall be regulated (hereinafter “Regulated Land Uses”) according to the Schedule of Regulated Land Uses attached hereto, marked Exhibit “B” and incorporated herein by reference.  When evaluating a use pursuant to Exhibit B and if such use may be considered to be within more that one Regulated Land Use category, such use shall be deemed to be the Regulated Land Use subject to greater restriction in order to further the purposes above.

Certain particular Regulated Land Uses shall be prohibited, or permitted only by Special Exception, within Zone 2 or Zone 3 as applicable, as set forth in the Schedule of Regulated Land Uses.

(c) The following uses are prohibited within the  Shrewsbury Borough Wellhead Protection Overlay District:

1)  Manufacturing and production of hazardous materials, excluding production for on-    site usage only.  These materials include any hazardous substance or hazardous waste as listed in the following federal regulations:

(a)	Superfund Amendments and Reauthorization Act (SARA) of 1986, Section 302 Extremely Hazardous Substances List (40 C.F.R. 300, App A and B);

(b)	Comprehensive Environmental Response Compensation and Liability Act Superfund (CERCLA) of 1980, Hazardous Substance List (40 C.F.R. 302, Table 302.4);

(c) SARA of 1986, Section 313, Toxic Chemical List (40 C.F.R. Section 372.45); and

(d) Resource Conservation and Recovery Act (RCRA) of 1976 and 1984 Amendments, Hazardous Wastes Lists (P and Y Categories) (40 C.F.R. Section 261.33 (e) and (f).  Note:  The lists referenced in Section B.1a, are summarized in the Title III List of Lists – Chemicals Subject to Reporting Under Title III of the Superfund Amendments and Reauthorization Action (SARA) of 1986, published July 1987, U.S. EPA

2)  Nuclear or radioactive materials or wastes.

3)  Wood-preserving operations using formulations of Chrome-Copper-Arsenate (CCC), pentachlorophenol (PENTA), and creosote and related chemicals;

4)  Battery recycling and reprocessing;

5)  Retail gas stations or truck stops;

6)  Agricultural application of halogenated volatile liquid organic pesticides (e.g., ethylene dibromide (EDB) and dibromochloropropane (DBCP), related chemicals and their commercial formulations);

- Processing, reprocessing and storage [and disposal] of PCB containing oils;

- Manufacturing and production of paving, roofing, and other construction materials, using asphaltic- and petroleum-based coating and preserving materials; and

Primary and secondary metal industries that manufacture, produce, smelt or refine            ferrous and non-ferrous metals.

10) Use List Not Exhaustive: The uses prohibited by this district represent the state of present knowledge and most common description of said uses.  As other polluting uses are discovered, or other terms of description become necessary, it is the intention to add them to the list of uses prohibited by this district.  These lists may be supplemented by amendment to this ordinance or by resolution.  To screen for such other uses or terms for uses, no use shall be permitted in this district without first submitting its building, site, and operational plans for Planning Commission review and Borough Council approval under this ordinance.

11) Changing Technology: The uses prohibited by this district are prohibited based upon the combined pollution experience of many individual uses, and the technology generally employed by that class of uses, which technology causes the uses as a class to be groundwater pollution risks.  As the technology of identified use classes changes to non-risk materials or non-risk methods, a person may petition for such a use to be reevalutated under this ordinance.  It shall be the responsibility of that person to retain a Licensed Professional Geologist with competence in the field of hydrogeology to provide data in support of such a petition.  The Petition shall be submitted to the Planning Commission for review.  Thereafter, the petition shall be evaluated by the Borough Council with assistance from the Borough Engineer, a Licensed Professional Geologist and/or other representatives of the Borough, as appropriate.  If the person demonstrates convincingly that the use no longer presents a pollution hazard, it may be allowed, but subject to any conditions that the Borough Council may attach to the use to further the purposes of this ordinance.  All Borough fees or costs arising out of or related to the petition shall be reimbursed to the Borough from the person who filed it.

SECTION 4.   REPORTING REQUIREMENTS

As to each lot or tract of land located within the Wellhead Protection Overlay District upon which there is conducted a Regulated Land Use, owner of record thereof shall submit, or cause to be submitted, to the Zoning Officer or any representative designated by the Borough, the following records and information in the manner prescribed:

a) Facility Profile Sheet  – Information to be submitted is as provided for on the Facility Profile Sheet, marked Exhibit “C” and incorporated herein by reference.  The Facility Profile Sheet must be completed on the form provided by the Borough, and available at Borough Offices, within 90 days of the enactment of this ordinance, and thereafter within 60 days of the biannual ordinance anniversary date.

b) Copies of all federal, state and county operational approvals, certificates, permits and applications, on-going environmental reports and monitoring results, relating to environmental, pollution control, hazardous substance and drinking water laws and regulations pertaining to such lot or tract of land, as and when required to be submitted to federal, state and county governments authorities.

c) In the event that any contaminants and/or substances regulated under federal, state or county environmental, pollution control, hazardous substance and drinking water laws and regulations are released on or from any lot or tract of land within the Wellhead Protection Overlay District, copies of any and all notices, reports and documents which such owner filed, or caused to be filed, with any federal, state and/or county governmental authorities which provide notice of or relate to such release, as when such notices, reports and documents are required to be filed with such governmental authorities; and

d) Copies of all notices, orders, rules, decisions, recommendations, enforcement actions and similar documentation, as and when received by or on behalf of such record owner or the occupant of any such lot or tract of land from any federal, state or county governmental authority in connection with the enforcement of environmental, pollution control, hazardous substance and drinking water laws and regulations.

SECTION 5.     ADMINISTRATION

- The Zoning Officer, or any representative designated by the Borough,  is hereby designated as the Borough official responsible for the administration and enforcement of this Ordinance.  The Zoning Hearing Board of the Borough shall hear appeals from the written determinations and orders of the Zoning Officer regarding applications, enforcement notices, cease and desist orders and other matters, and shall also hear substantive and procedural challenges to the validity of this Ordinance.

- Uses of lots or tracts of land in existence on the date of enactment of this Ordinance which are Regulated Land Uses shall be deemed to be “non-conforming uses” of land under the terms of this Ordinance.  Such non-conforming uses of land may be continued by the present or any subsequent owner as long as:

(1) Such use is and remains otherwise lawful and in compliance with all  federal, state and county environmental, pollution control, hazardous substance and drinking water laws and regulations;

(2) Such non-conforming use has not been and is not discontinued for a period of six (6) consecutive months;

(3) Such non-conforming use is not, after the date of enactment of this Ordinance, materially altered, changed or expanded;

(4) The record owner of the lot or tract of land on which such non-conforming use is located is in compliance with Section 4 of this Ordinance regarding reporting requirements;

(5) Such non-conforming use is not an actual known source of groundwater contamination;

(6) A Facility Profile Summary is submitted to the Borough biannually as described under Section 4(a); and

(7) Such use shall upgrade its technology on a regular basis, as the technology required by applicable law is changed, or upon request of the Borough, in order to minimize the risk associated with such use to the community water resources.

c) A Regulated Land Use shall be deemed to be new or materially altered, changed or expanded if:

  - The land use which constitutes the Regulated Land Use was not previously present and conducted upon the lot or tract of land in question;

(2) The production and/or storage capacity of the Regulated Land Use

is increased;

(3)	The types of any substances which give rise to the Regulated Land

Use are changed;

- The number of types of substances which give rise to the Regulated Land Use are changed;

- The quantity of any substances which give rise to the Regulated Land Use is materially increased; or

- The land area subject to the Regulated Land Use is enlarged in any respect.

d) Following the date of enactment of this Ordinance, Regulated Land Uses which are new or which constitute material changes, alterations or expansions of nonconforming Regulated Land Uses will be prohibited in accordance with the terms of section 3(c) above or Exhibit “B” annexed hereto, thereby prohibiting such Regulated Land Uses, or permitting such Regulated Land Uses only upon the granting of a Special Exception.  Any Regulated Land Use which is permitted to be conducted within the Wellhead Protection Overlay District as a result of the granting of a Special Exception in accordance with the terms of this Ordinance shall not be deemed to be a non-conforming use of land under the terms of this Ordinance, but shall without further action be considered a land use which is in conformity with the terms of this Ordinance.

(e) As to any new Regulated Land Use or any proposed alteration or expansion of a non-conforming Regulated Land Use, and as to which such Regulated Land Use is permitted within the applicable Wellhead Protection Zone upon the granting of a Special Exception, such Special Exception shall only be granted upon the following conditions:

- Such Regulated Land use is one which is specifically authorized as a Special Exception use in the Wellhead Protection Zone in question, as set forth in Exhibit “B” ; and

- Such Regulated Land use will not, during construction or thereafter, cause the degradation of the groundwater quality upon or beneath the lot or tract of land in question, or upon or beneath adjacent lots or tracts of land, the degree and extent of which degradation is or would be violative of safe drinking water standards promulgated by federal, state or county governmental authorities; and

- Satisfactory evidence has been provided to the Borough’s Zoning Officer; or Zoning Hearing Board, as applicable, that the proposed Regulated Land Use is in compliance with all federal, state and county laws and regulations applicable to such Regulated Lane Use and the record owner or occupant has received all necessary approvals of federal, state and county governmental authorities for the conduct of such Regulated Land Use.

f)	Application for a Special Exception shall be made to the Zoning Hearing Board of the Borough in writing on such form as may be prescribed by the Zoning Officer and approved by Resolution of the Borough Council and such application shall include, at a minimum, a detailed description of each of the activities to be conducted upon the lot or tract of land in question which constitute a Regulated Land Use, including a listing of all substances which are to be stored, handled, used or produced in connection with each Regulated Land Use being proposed and which substances are subject to regulation by federal, state and/or county governmental authorities.

g)	The Zoning Hearing Board of the Borough shall issue a written determination approving or disapproving the application for a Special Exception, or conditioning the granting of the Special Exception upon adherence to any or all of the following requirements by the applicant for the Special Exception, where the Zoning Hearing Board has found that such adherence is reasonably necessary to fulfill the groundwater protection purposes of this Ordinance;

      - The installation of Borough-approved containment facilities and systems so as to prevent the contamination of groundwater by substances regulated by federal, state and/or county governmental authorities.

      - The preparation, filing (with the Zoning Officer) and periodic revision of an emergency plan addressing the means by which any potential contamination of groundwater will be controlled, collected and remediated, including emergency contacts and identification of potential contaminants;

      - Regular inspection and/or monitoring by the owner, occupant, the Zoning Officer and/or third parties, of the Regulated Land Use area;

4. Compliance by the applicant with the provisions of the Borough Subdivision and Land          Development Ordinance then in effect pertaining to sanitary sewage disposal, water supply, storm water management and easements.

(h) A Facility Profile Summary is submitted to the Borough Biannually as described under Section 4(a)

(i) Other items that may be required to characterize environmental or physical conditions of the subject property.

1)	Applications to the Zoning Hearing Board of the Borough for a Special Exception under this Ordinance, as well as written determinations of the Zoning Officer and appeals from the written determinations of the Zoning Officer to the Borough Zoning Hearing Board and appeals to the courts of the Commonwealth of Pennsylvania, shall be subject to the same procedural (but not substantive) rules as are applicable to applications for special exceptions under the terms of the underlying Zoning Ordinance of the Borough in effect at the time the application is filed.

SECTION 6.   MAJOR SUBDIVISION AND LAND DEVELOPMENT PLANS

All major subdivision proposals and other proposed new development plans to be located within the Wellhead Protection Overlay District shall be reviewed by the Zoning Officer and the Borough Planning Commission for compliance with the provisions of this Ordinance.  It shall be the responsibility of the Zoning Officer and the Borough Planning Commission to recommend approval, disapproval or approval with conditions or modifications, of the proposed subdivision or development plan, so as to assure compliance with the provisions of this Ordinance.

- Subdivisions and land developments within  Zones 1, 2 or 3 for which storm water management controls are required pursuant to the Borough Subdivision and Land Development Ordinance shall be designed consistent with the following:

  - Storm water retention basins shall be prohibited;

  - Storm water detention basins shall be prohibited from Zone 1, and within Zone 2 shall be designed with an impermeable liner to prohibit the infiltration of impounded water to the subsurface.

- Subdivisions and land developments within Zones 1, 2 or 3 as mapped on Exhibit “A” shall have the following Preliminary Plan requirements in addition to those requirements of the Borough Subdivision and Land Development Ordinance:

  - A recognized Licensed Professional Geologist employed by the developer with competence in the field shall review aerial photographs, soils, geologic and other available related data as the data relates to the subject property.  The licensed Professional Geologist shall also conduct a site inspection of the property and submit a report of the site to the Borough.

  - Based on the work required in Section 6(b)(1), the professional geologist shall prepare a map not less than scale, 1” = 100 ft. of the site showing all topographic, geologic and other pertinent physical features.  The mapping shall indicate, but shall not be limited to, the following:

    - Closed depressions

    - Seasonal high water table indicators

    - Outcrops of bedrock

    - Surface drainage into ground

    - Lineaments and faults

    - Quarries and mines

    - Oil, gas or water wells (active or abandoned)

    - Geologic contacts

    - Springs, seeps or wetland areas

    - Distance and direction of nearest public or adjacent private water supply well

  - Based on the work performed in Sections 6(b)(1) and 6(b)(2), Shrewsbury Borough shall determine what if any further testing should be done by the applicant to ensure compliance with this Ordinance.  Testing methodology shall be reasonable under the circumstances, including (i) the scale of the proposed development, and (ii) the hazards revealed by examination of available data and the site inspection.

  - The applicant shall cause the additional testing established in Section 6(b)(3) to be done.  A study report shall be submitted and referred to the Borough Engineer.  This study shall include a map of the area, all test results and a recommendation on the mitigation measures to be taken.

  - The Borough Engineer shall report to the Planning Commission, with a copy to the landowner, his or her opinion as to the adequacy of the study and as to the capability of the site to support the proposed development in a manner in which the risks attendant to the development in areas are either eliminated or minimized.  Recommendations for site development including building location may be included.  Additional studies or testing as deemed necessary by the Borough Engineer in order to produce an adequate study given the scale of the proposed development and the hazards revealed may be required of the applicant.

SECTION 7.     GENERAL EXCEPTIONS

The following General Exceptions specify those land uses and activities that are permitted by right and do not require a Special Exception:

- Transit:  The transportation of any hazardous or governmentally regulated substance through the Wellhead Protection Overlay District shall be exempt from provisions of this Ordinance, provided that the transporting vehicle is in transit through the Wellhead Protection Overlay District and further provided that such transportation is conducted in compliance with all applicable federal and state laws and regulations;

- Residential: To the extent otherwise permitted or regulated by federal, state and/or county statutes and regulations, the owners and/or occupiers of lots and tracts of land which are primarily utilized for the purpose of single or multi-family residential dwellings are permitted to utilize and store fuels, hazardous chemicals, pesticides, fertilizers, inflammable liquids and gases, and toxic and regulated substances in such quantities and in such manner as is associated with normal and responsible  household use, and such limited utilization shall not be deemed a Regulated Land Use for the purpose of this Ordinance.  This exception does not apply to underground liquid fuel storage tanks.

SECTION 8.    PREVENTIVE AND ENFORCEMENT REMEDIES

For the purpose of preventing violations of this Ordinance and enforcing the provisions of this Ordinance, the Borough shall have available to it the same preventive and enforcement remedies, including the use of civil actions, as are set forth in the Zoning Ordinance of the Borough in effect from time to time.  In addition, the Zoning Officer of the Borough is authorized to issue cease and desist orders whenever such Zoning Officer becomes aware of violations of this Ordinance.  The Zoning Officer is authorized to issue Enforcement Notices with respect to violations of this Ordinance, such Enforcement Notices to be issued in accordance with the Enforcement Notice provisions of the Zoning Ordinance of the Borough in effect from time to time.  Finally, Shrewsbury Borough may seek an injunction to prevent any action that it reasonably believes may constitute irreparable harm to the Shrewsbury Borough water sources, and such an injunction may be obtained without posting a bond therefore.  When invoking the preventative or enforcement remedies to this Ordinance, Borough shall be entitled to recover all costs incurred, including, but not limited to, attorney’s fees, costs of suit and inspection or investigation fees.

SECTION 9.   FEES

The Borough Council shall, from time to time, establish by resolution a schedule of fees, charges and expenses and collection procedures for Special Exceptions, costs of review and inspection, appeals and other matters pertaining to this Ordinance.  The schedule of fees shall be available for inspection in the Municipal Office of the Borough.  An application will not be considered to be complete until all applicable fees, charges and expenses have been paid in full.  In addition to such fees, the applicant shall pay any and all Borough costs or fees arising out of or related to this ordinance and the enforcement thereof.

SECTION 10.   VIOLATIONS

INSERT ENFORCEMENT LANGUAGE AND PENALTIES

SECTION 11.    MISCELLANEOUS

- Conflicts:  Whenever there is a difference between any of the minimum standards specified in this Ordinance and any standard included in any other ordinance, law or regulation of the Borough, the more stringent requirement shall apply. The provisions of this Ordinance shall be deemed to be supplementary and in addition to the provisions of the Zoning Ordinance and Subdivision and Land Development Ordinance of the Borough as each is in effect from time to time.

- Severability:  The provisions of this Ordinance are severable, and should any article, section, subsection, paragraph, clause, phrase or provision of this Ordinance be declared by a court of competent jurisdiction to be invalid, such judgment shall not affect the validity of this Ordinance as a whole or any part or provision thereof other than the part so declared to be invalid.

- Effective Date:  This Ordinance shall become effective as provided by law.

(d)  Repealer:  All prior Ordinances that are inconsistent herewith are hereby repealed to the extent of such inconsistency.

ENACTED AND ORDAINED by the Borough Council of Shrewsbury Borough this 			day of 					, 20	.

ATTEST:						BOROUGH OF SHREWSBURY

Secretary						(Vice) President

Approved this		day of 					, 20	.

James W. Reedy, Mayor